I. Before You Leave The Yard

1.  Safety Alert Symbol And Signal Word Explanation

1.1                                        The triangle with the exclamation point inside is used to alert you to an important safety point, and is called a Safety Alert Symbol. One of the following color-coded signal words will appear after the safety alert symbol:

DANGER WARNING

NOTICE

CAUTION

or - without the symbol:

CAUTION

is replaced by:

• If the safety alert symbol is followed by the signal word DANGER with white letters in a red box (      DANGER  ), it indicates a hazardous situation which, if not avoided, WILL lead to death or serious injury.

• If the safety alert symbol is followed by the signal word WARNING with black letters in an orange box (       WARNING   ), it indicates a potentially hazardous situation which, if not avoided, COULD result in death or serious injury.

• If the safety alert symbol is followed by the signal word CAUTION with black letters in a yellow box (      CAUTION    ), it indicates a potentially hazardous situation which, if not avoided, COULD result in minor to mod-

erate injury.

• The signal word CAUTION, used in a yellow box, but without the safety alert symbol (  CAUTION  ), means the point addresses a hazard which, if not

avoided, COULD cause damage to equipment or property.

• The signal word NOTICE   NOTICE , now replaces the signal word caution above.

2.  What To Do Before You Arrive At Work

2.1	Get enough sleep to be ready for the day’s work. Accidents can happen when the body is on the job, but the mind is not.

Dress in appropriate apparel and Personal Protective Equipment (P.P.E.). You should always wear these items when pumping concrete (Including *full face shield or * breathing mask where necessary as shown in Figure 1):

• hard hat

• safety glasses or goggles (*Full face shield when shotcreting)

• snug fitting clothes

• gloves

• steel toed shoes

In addition, you should wear:

• hearing protection if you stand near the pump or any other source of noise.

• breathing mask when mixing slurry or whenever there is cement dust in the air

• rubber gloves during cleanout

• rubber boots anytime you have to stand in concrete

Jewelry, athletic shoes, sandals, and shorts are examples of clothing that should

NOT be worn when pumping.

*   Breathing mask needed when cement dust (or other toxic dust) is present in the air.

* Full face shield should be used when shotcreting or any time material is rebounding.

Hard Hat

Safety Glasses

Full Face

Shield*

Breathing

Mask*

Safety Vest

Snug-fitting

Clothes

Work Gloves

or Rubber Gloves

Hearing

Protection

Figure 1

Personal Protective

Equipment (P.P.E.)

Steel Toed Shoes or

SafeGear_wVestNomask.eps

Finisher’s Boots

2.2                                               WARNING   Be sure that any clothing you wear does not have strings, fringes, or other external tightening means that could be caught in moving parts (Figure 2).

This is a hazard!

Knot and cut off excess string

Figure 2

No strings attached

Safewntr.eps

2.3	Arrive to work on time. Accidents can be caused by hurrying through procedures.

2.4                                               WARNING   Never go to work on a construction site or work on, around or near a piece of machinery when under the influence of drugs or alcohol. Beware of prescription medications or “over the counter” drugs, many of which have spe- cific warnings about operating machinery after taking the medication (Figure 3).

NO!

nodrugs.eps

Figure 3

Your co-workers depend upon you for their safety

2.5                                               WARNING   Don’t bring your personal problems to work with you. In an office setting this may be annoying to co-workers, but on a construction site it can be deadly. The workers around you depend on you for their safety.

3.  What To Check Before You Leave The Yard

3.1                                               WARNING   Do not operate the machine until you read and understand the unit’s operation manual. Lack of understanding of proper operating procedures could result in unsafe operation. Operation manuals are issued with each new unit. If you haven’t seen it, ask your supervisor. Replacements are available from the manufacturer.

3.2                                               WARNING   Inspect delivery pipes, concrete delivery hoses, and end hoses for wear. Never use a hose or pipe that is dented or worn out. Know the maxi- mum pressure that your machine can exert on the concrete, and be sure that the pipes, hoses and clamps are capable of handling the pressure. Maximum pressure on concrete is stated in operation manuals, service manuals, and on the serial number plate of the machine. A chart showing the minimum wall thickness of pipeline versus maximum pressure is found on page 51 in the appendix section of this Safety Manual.

3.3                                               WARNING   If you will need to use compressed air to clean out the system pipeline, BE SURE that you have the proper training, equipment, and attachments to do this procedure safely! Proper attachments include:

• A blow out head with properly sized air discharge regulator valve and sepa- rate water/air inlet. The two openings should be spaced apart far enough that a blowout ball could not cover both openings at once.

• A go devil, or a hard sponge ball. Regardless of which is used, it must fit into the pipeline tight enough that air cannot escape ahead of it.

• A ball or go devil catcher that will catch the go devil or ball when the line has been purged of all concrete, unless another method of controlling the outlet is used. There are two types of catchers (see paragraph 5.23 on page 17).

• A hose that is rated for the pressure of the air compressor you will use and that is able to connect with both the air compressor and the blow out head. The hose must be in good working condition and must be free of cracks, frays, tears or other damage. Do NOT improvise on this. Make sure that you have the right part (Figure 4).

Water/air inlet

Air inlet regulator valve

Air discharge regulator valve

blow out head

Figure 4

ball catcher

Compressed air accessories

3.4                                               WARNING   Be sure that the unit is equipped with all the pipes, clamps, gas- kets and hoses, blow out adapters, ball catchers, and other accessories that you will need for the day’s work. “Making do” with inappropriate equipment could cause accidents.

3.5                                        On trailer mounted units, check the oil and cooling system (air or water cooled systems) of the pump drive engine. Accidents could occur when lack of mainte- nance is causing a distraction while operating the equipment.

3.6                                        Be sure the battery has enough charge to start the pump drive engine. You will be rushed on the job if you have to do repair work before you can begin operation.

3.7                                               WARNING   The operator is responsible for checking to see that the concrete pump, and delivery system are in safe and proper working condition. If an unsafe condition exists, work must not begin until necessary repairs have been com- pleted, or until the machine can be operated safely.

3.8                                               WARNING   The operator is responsible for checking that all safety equip- ment and guards are in place and in good condition. If found to be missing, incom- plete, or damaged, work must not begin until the situation has been made safe.

3.9                                               WARNING   The operator is responsible for checking that all safety decals are in place and are in readable condition. If found to be missing or unreadable for any reason, steps should be taken to obtain replacements.

3.10                                             WARNING   Inspect the tires and brakes on the truck. Never drive a truck with bald or cracked tires, or with weak or worn brakes. If you have air brakes, be sure that the air system is free from leaks and will maintain pressure when driving. Loss of air pressure will cause the brakes to be applied while driving. If driving continues after the brakes are applied, the resulting friction could cause enough heat to start a fire.

3.11	Drain moisture from the air tanks that supply the unit’s brakes (if so equipped).

This is especially important if weather conditions could cause the moisture to freeze. If you lose air pressure because of frozen moisture, the brakes will apply themselves, and you will have to stop driving until the unit is repaired.

3.12	WARNING  (See Figure 5.) Mount or dismount the pump or truck using the

3 Point Rule (i.e. keep two hands and one foot or one hand and two feet in contact with a secure surface at ALL times).

safestep.eps

Figure 5

The 3 Point Rule

3.13                                             WARNING   Never mount or dismount the truck or pump while carrying objects that prevent you from using the “3 Point Rule.” Move the objects sepa- rately, if needed.

3.14                                             WARNING   If applicable, be sure that outriggers are pinned and locked before traveling. If the locking device is damaged or worn, it should be repaired immediately and the unit must not be driven until the outriggers can be posi- tively locked against accidental opening.

3.15                                             WARNING   Be sure there is nothing in the cab of the truck (such as empty soda cans, loose tools, etc.) that could interfere with the operation of the vehicle.

3.16                                      Be sure that all road-related safety devices (warning signs, flares, fire extin- guisher, etc.) are present and secured for travel.

3.17                                      Be sure all personal protective equipment (hard hat, safety goggles, rubber gloves, etc.) are secured for travel.

3.18                                             WARNING   Be sure the windshield and mirrors are clean and free of frost or ice, and that the mirrors are properly adjusted.

3.19                                             WARNING   Verify that head lights, tail lights, turn signals, brake lights, backup warning horn, and backup lights are operational.

3.20                                      In some cases you may be asked to operate a machine other than the one with which you are familiar. In these cases, be sure to:

• Know the weight, height, and width of the machine.

• Have a copy of the operation manual with you.

• Ask the machine’s normal operator, the dispatcher, or your supervisor ques- tions regarding any unusual or unique operational characteristics of the machine.

•  Familiarize yourself with the machine by setting it up in the yard and running the functions, and by familiarizing yourself with the operation manual. This is especially important if the new machine is significantly different than the one you normally operate. Your co-workers depend on you to know the machine.

3.21                                             WARNING   Be certain that all loose items on the unit are secured for travel before driving.

3.22                                             WARNING   Emergency stop switches should be periodically checked by activating the switch in the yard and confirming that none of the pump functions operate electrically or manually.

4.  Safety Rules For Towing Trailer Mounted Concrete Pumps

4.1                                               WARNING   Be sure the towing vehicle is heavy enough and has enough horsepower and braking ability to tow the trailer. This is critical to maintaining control at highway speeds and to braking ability. If the trailer is heavier than the towing vehicle, braking distances will be greatly increased (Figure 6).

trlrbg.eps

Figure 6

Do not under size the towing vehicle

NO!

4.2                                          NOTICE Never drive the unit with concrete in the hopper. The extra weight in the back of the machine will remove weight from the tongue and cause the unit to fishtail.

4.3                                               WARNING   Check the tires, tire pressure, and brakes on the trailer before towing. Never tow a vehicle with cracked or bald tires. A trailer tire blowout can cause loss of control in the towing vehicle.

4.4                                               WARNING   Be especially careful on ice or slippery roads when towing a trailer. A skid that would normally be easily correctable can be multiplied by the trailer, causing loss of control.

4.5                                               WARNING   Be sure that the electrical connections between the towing vehi- cle and the trailer are sturdy and reliable, and that the lights on the towing vehicle and trailer are working.

4.6                                               WARNING   Always use safety chains and break-away protection when tow- ing a trailer.

4.7                                           CAUTION   Be aware of local or state regulations regarding mirrors and lights when towing a trailer.

4.8                                               WARNING   When  towing  a  trailer,  your  stopping  distance  and  turning radius are greatly increased. Be aware of this at all times.

4.9                                               WARNING   When towing a trailer long distances, it is important to check the hitch, wiring, and safety chains frequently.

4.10                                             WARNING   Be aware of your length when towing a trailer. A common cause of trailer accidents is turning too close to curbs or objects.

4.11	WARNING  Never back up a trailer without a guide.

4.12                                             WARNING  Frequently observe the trailer and watch for unusual swerving or indications of problems, such as a flat tire.

II. On The Job Site - Safety Rules For Job Setup

5.  Setting Up A Trailer Mounted Pump and/or A Separate Pipeline

5.1                                        The job setup phase sets the stage for most accidents. Taking a few extra moments to correctly set up the job will improve your chances of having a safe, trouble free day.

5.2                                        The operator is responsible for the safe operation of the machine. Notify your employer, the job superintendent, and/or O.S.H.A. if you are being asked to set up in an unsafe manner. You are never required to take a chance with safety. You are the only person who can determine that the job circumstances under your con- trol are safe.

5.3                                               WARNING    Any power connections above 24 volts must be made by a licensed electrician. The supply power and appropriate disconnect boxes are the responsibility of the contractor.

5.4                                               WARNING   Electrical power on the job site may be taken only from a fused, grounded disconnect box with a disconnect switch that can be locked against activation. If you will be making repairs to the concrete pump or separate placing boom, first lock out the power at the disconnect box.

5.5                                               WARNING   On  units  equipped  with  electric  motors,  check  the  power cables every day. If they are frayed or have open spots in the insulation, replace the wire. If the connectors are worn or loose, have repairs made by a licensed elec- trician.

5.6                                               WARNING   Consider the safe approach and departure of the ready-mix trucks and adjust your setup accordingly. Adjusting your setup position by a few degrees one way or another could mean the difference between a safe approach and an unsafe approach. Some examples of unsafe approaches are: too near an excavation or sticking out into traffic.

5.7                                               WARNING   Avoid collisions! Secure the immediate area of the machine from public traffic in accordance with all applicable regulations (warning lights, safety cones, barricades with flashers, etc.).

5.8                                               WARNING   Pipelines, end hoses, couplings, and all other material delivery components must be able to withstand the maximum concrete pressure of the pump. Be sure of it! Read and understand the minimum wall thickness chart found in the Appendix of this manual. If you don’t understand the chart, contact the pipe manufacturer for assistance.

5.9                                               WARNING   Do not use a piece of pipeline, end hose, coupling, or any other material delivery component that is not in good condition. Replace, do not repair damaged pipes and hoses. Concrete pipeline system is subject to wear, and the rate of wear is affected by pumping pressure, concrete composition, pipeline material, and other factors. Read and understand the minimum wall thickness chart in the Appendix of this manual. Bursting pipes and concrete escaping under pressure is a serious safety hazard! (See Figure 7)

Figure 7

Delivery system components must be able to withstand maximum pump pressure

5.10                                      When laying out a pipeline, it is preferable to use an elbow instead of a hose to make direction changes. Elbows have less resistance to flow than hoses, and will therefore reduce the overall pressure required to push the concrete.

5.11                                      Always use the largest diameter pipeline that is practical, and use steel pipe instead of rubber hose. This will keep the pressure required to push the concrete to a minimum.

5.12                                      Support the delivery pipeline. Either an “S” transition pipe should be used to bring the pipe to ground level, or each section of the pipeline should be supported at the pump outlet level.

5.13                                             WARNING   The sections of pipe nearest the pump are subjected to the high- est pressure and the greatest wear. Because of this increase of pressure near the pump, you should install only thick walled pipe, in “like new” condition there. Read and understand the minimum wall thickness chart in the Appendix of this manual.

5.14                                             WARNING   The maximum concrete pressure of the pump must be the only factor used to determine what thickness of pipe and what type of ends are needed. In the case of a rock jam or any other type of blockage, the maxi- mum pressure of the pump will be exerted.

5.15                                      Grooved (Victaulic) ends are not recommended for concrete pumping. Read and understand the comparison between heavy duty raised, metric, and grooved ends in the Appendix of this manual.

5.16                                             WARNING   If the pipeline remains on the job (as is the case when pumping a high rise building), the operator is responsible for checking the pipeline for dents, cracks, wear, and continuity each day before the pour begins.

5.17                                             WARNING   In vertical runs, the weight of the vertical sections of pipe must be supported by a thrust block (often called a deadman, Figure 8) or other load- bearing device. Each section of pipeline in a vertical run must be secured from lateral and horizontal movement.

Lateral movement restraint

Thrust block

(deadman)

deadman2.eps

Figure 8

A thrust block (deadman)

5.18                                             WARNING   If you will be unable to see the point of placement, establish a system of communications with the workmen who will be there. Arrange for radio communications, a system of visual or auditory signals (lights or bells), or a spot- ter (Figure 9). If a spotter is used, agree on hand signals before beginning the pour!

trlrsptr.eps

Figure 9

Arrange communications before starting

5.19                                             WARNING   Never leave the machine unattended when it is running or ready to run. If you must leave the area, you must leave someone to monitor the unit. This is especially critical if there are children in the vicinity.

5.20                                             WARNING   Watch for children! It is possible for children to access the machine, but it is not safe for them to do so.

5.21                                             WARNING   If spectators will be near the job, cordon off an area where they will be safe.

5.22                                             WARNING   If you will be cleaning the pipeline with compressed air at the completion of the job, be sure that you have all the necessary accessories to do the job safely. If you don’t have all of them, make arrangements to get them before you begin to pump. Do not improvise on this. Make sure that you have the right parts. The minimum accessories include:

• A blow out head with properly sized air discharge regulator valve, and sepa- rate water/air inlet. The two openings must be spaced apart far enough that a blowout ball could not cover both openings at once.

• A go devil, or a hard sponge ball. Regardless of which is used, it must fit into the pipeline tight enough that air cannot escape ahead of it.

• A ball or go devil catcher that will catch the go devil or ball, or some other method of controlling the discharge while the line is being purged of material. There are two types of catchers (see paragraph 5.23).

• A hose that is rated for the pressure of the air compressor you will use and that is able to connect with both the air compressor and the blow out head. The hose must be in good working condition and must be free of cracks, frays, tears or other damage.

• If you will be cleaning the pipeline with compressed air at the completion of the job, be sure an adequate air compressor is available before starting the job.

• If you will be cleaning a vertical pipeline with compressed air at the comple- tion of the job, you must have a shutoff valve or switching valve installed at the bottom of the vertical run!

Water/air inlet

Air inlet regulator valve

Air discharge regulator valve

Figure 10

Ball catcher and blow out head

blow out head

ball catcher

catcher you are using. You may need to adjust your clean out procedure according

to which type you have. The two types are as follows.

1.   Catchers that stop the ball or go devil before air can escape, and

2.   Catchers that allow the air out of the pipeline after the ball or go devil has reached the end.

Each type of catcher has advantages and disadvantages (Figure 11).

ctchrexplnsm.eps

1

AIR PRESSURE

Advantage: There is no turbulent expulsion of air.

Disadvantage: Air remains in the line, because it cannot pass the go devil. The line must not be opened until all air is drained at the

blow out head.

2

AIR

Advantage: All compressed air is relieved with the expulsion;

the pipe may be opened immediately.

Disadvantage: There will be a turbulent expulsion as the air escapes.

Figure 11

Types of catchers

With catcher type 1, the go devil stops, but air is still trapped behind it. The advan- tage is prevention of the sometimes violent expulsion of air at the end of the pipe. The disadvantage is that the air must be drained from the blow out head before the pipe line is safe to open. The pipeline must be controlled; allow no one to open it until all compressed air is relieved.

Catcher type 2 is long enough that the compressed air escapes behind the go devil. Note! This would happen with either catcher when used with a ball instead of a go devil. The advantage of this is that once you hear the turbulent expulsion, there is no pressurized air remaining in the line, and the line may be opened immediately. The disadvantage is the expulsion itself. In this case, the end of the line must be controlled because flying concrete and aggregate pose a hazard.

Both catchers can be safely used if care is given to the hazards involved.

III. Concrete Pump Operation

6.  Safety Rules For Pump Operators

6.1                                               WARNING   Only qualified operators are allowed to operate the pump. A “Qualified Operator” is defined as someone who:

• has reached the age of 18 years (21 for interstate travel),

• is physically and mentally capable,

• has been trained in the operation and maintenance of the pump and the plac- ing boom (if applicable),

• has demonstrated his/her capabilities to the employer in respect to the opera- tion and maintenance of the pump and placing boom (if applicable), and

• can be expected to perform these duties, as assigned, in a reliable manner.

6.2                                               WARNING   Because the operator is responsible for the safe operation of the machine, it is crucial that he/she understands the proper operation of the machine and the safety rules that apply to the job at hand, so the course of action taken in unforeseen circumstances will be a safe one. Only thorough training and super- vised job experience can supply the necessary understanding.

6.3                                               WARNING   When  operating  the  machine,  wear  Personal  Protective Equipment. (Including *full face shield or * breathing mask where necessary.) (Figure 12)

* Needed when exposed to airborne cement particles (or any other toxic dust).

* Full face shield should be used when shotcreting or any time material is rebounding.

Figure 12

Wear Personal Protective Equipment (P.P.E.)

during operation.

6.5                                               WARNING   Electrocution  hazard!  If  you  are  operating  and  lightning moves into the area, seek shelter until the lightning is gone.

6.6                                               WARNING   Crushing hazard! Never, ever position yourself between a ready mix truck and the pump! Stand off to the side, so the ready mix driver can see you at all times (Figure 13).

backsig.eps

NO!

Figure 13

Clear Signals

YES!

Never stand between the ready mix truck and the pump

Use clear and concise hand signals

6.7                                               WARNING   When backing in ready mix trucks, use clear and concise hand signals (Figure 13).

6.8                                                DANGER    Loss of  hearing! While standing near a  working concrete pump, sound pressure levels may exceed O.S.H.A. standards for constant expo- sure (Figure 14).

PERMISSIBLE NOISE EXPOSURES*

*Under part 1910.95 “Occupational Noise Exposure,” (Dept. of Labor) of the Code of

Federal Regulations, Chap. XVII of Title 29 (39 F.R. 7006).

| DURATION per DAY | Sound level in dB (A) |
| --- | --- |
| in HOURS | Slow response |
| 8 | 90 |
| 6 | 92 |
| 4 | 95 |
| 3 | 97 |
| 2 | 100 |
| 1 1/2 | 102 |
| 1 | 105 |
| 1/2 | 110 |
| 1/4 or LESS | 115 |

††

Figure 14

Noise level and exposure time limits

6.9                                               WARNING   Do not let the concrete level in the hopper become low! If air is sucked into the material cylinders, the pump will compress the air. Compressed air always poses a hazard as it is expelled from the hopper or the delivery pipeline (Figure 15). If air is taken into the material cylinders, take the following steps to minimize the hazard:

1.   Stop the pump immediately. Hit the emergency stop button if that is the quickest way to stop the pump. There will be an expulsion of compressed air the next time the concrete valve shifts, which can be safely absorbed by filling the hopper with concrete.

2.   If possible, fill the hopper with concrete to just below the grate, then pump slowly in reverse for several strokes. This will not remove all the air, but it should minimize the amount left in the pipeline.

3.   Persons standing at the discharge end or near the delivery line must be warned to move away until all of the air has been purged. Personnel should move a prudent and reasonable distance beyond the end-hose movement area or the point of discharge, and personal protective equipment (PPE) should be worn (Figure 15).

4.   When the pump is restarted, pump forward slowly until all air is removed from the pipeline. Don’t assume that the first little air bubble is the end of the compressed air.

5.   Do not allow anyone near the discharge until concrete runs steadily from the end and there is no movement of the delivery system.

If workers are positioned in high or precarious places, warn them to expect a loud sound as the air escapes the pipeline. (Warn them even if they are well away from the discharge.) That way, we can prevent the worker from falling as a result of being startled by the noise.

hosepop3.eps

Figure 15

Remove everyone from the discharge area whenever air is in the line

6.10	WARNING	Air can be introduced into the delivery system in several ways.



For example:

• when initially priming the delivery system,

• when restarting after moving,

• when restarting after adding or removing delivery system

• when attempting to remove a blockage by “rocking” the concrete,

• when pumping is stopped and the pipeline is at a downward angle

6.11                                             WARNING   When initially priming the delivery system, when restarting after moving, when restarting after adding or removing hoses, when attempting to remove a blockage by “rocking” the concrete, or whenever air has been intro- duced into the line, warn everyone to stay away from the discharge until material runs steadily. Personnel should move a prudent and reasonable distance beyond the end-hose movement area or the point of discharge, and personal protective equip- ment (PPE) should be worn (Figure 15).

6.12                                             WARNING   Blockages in the pump or delivery pipeline can create an unsafe condition. Blockages are caused by many different factors, as outlined below.

CAUSES OF BLOCKAGES

• Faulty concrete mix design. The concrete that is being supplied may not be a pumpable mix, for example there may be too much sand or too little cement. There may be bleeding or segregation. Some admixtures adversely affect pump- ability (e.g., too much air entrainment). If the mix is not pumpable, no amount of operator expertise will make it so.

• The line size may be inadequate. The line size should always be at least 4 times larger than the largest aggregate being pumped, or blockages could occur.

• Worn concrete valve parts. Worn parts allow the finest material and water to escape back into the hopper when pressure is applied.

• Pipeline and joint deficiencies. This would include dirty pipes (pipes that have not been cleaned properly), worn and leaking pipe joints that allow loss of con- crete fines and water, pipes that haven’t been properly primed before starting, and too many sections of rubber hose, which increases friction. These are all causes of blockages that can be controlled by the operator.

• Pump inadequate for the application. The pump selected for the job may not have enough pressure or horsepower available for the required duty.

• Concrete setting up in the pipeline. This may be caused by delays on site (e.g., repairing a broken form), or by attempting to pump “old” concrete (concrete that was batched hours before pumping and is being kept alive only by adding water and constant agitation). Weather conditions can also affect how quickly the con- crete becomes hard. Companies should establish procedures for these situations. A good rule of thumb is: If in doubt...wash out.

• Foreign matter in the concrete. Pieces of old concrete that break away from mixer fins, unmixed clumps of cement, mixer fins, hammers, and furry mam- mals are examples of foreign matter that have caused blockages.

• An inexperienced operator can cause blockages by setting up the job improperly. For example, if the placing crew is forced to add hose or pipe to reach a far point after the pour is already in progress, there is a great chance of creating a blockage due to the dry conditions inside the pipe or hose. It is for this reason that the job should be set up so pipe or hose need only be removed (never added) as the day progresses. If dry pipe or hose must be added, it must be lubri- cated just like the rest of the pipe was lubricated when you first started.

• An inexperienced or improperly trained placing crew can cause blockages by kinking the end hose. This type of blockage can lead to serious accidents because the hose may un-kink by the force of the pump.

• The concrete becomes segregated in the hopper.

a. If the concrete is too wet, the cement and fine material get washed from the stone and course sand. This mix will not pump. It is for this reason that you should cover the hopper as you wait out a passing storm, never allow a truck mixer to wash out in your hopper, and never add water to the mix.

b. If concrete is over vibrated, it will separate. Turn off the hopper vibrator when not actively pumping.

6.13                                             WARNING   Never try to remove a pipeline blockage by applying high pres- sure to it, because that will cause the blockage to become a plug. If you have a blockage, immediately stop the pump. Stroke the pump several times in reverse. Slowly stroke the pump in forward, and try to dislodge the blockage. If you are moving the blockage, continue to do so slowly and gently. While attempting to clear the blockage, remove all personnel from the discharge area, as air may be introduced into the placing line during this process. If you are unable to move the blockage after a couple of attempts, stop the pump. Continuing to apply high pres- sure could create a hazardous condition.

6.14                                             WARNING   If the pump or associated equipment develops a problem that creates an unsafe condition, you must stop pumping immediately! Do not restart until the unsafe condition has been remedied.

6.15                                             WARNING   The following points must be observed when locating a block- age.

• Pump in reverse for at least two strokes, then stop the pump. Do not allow anyone to open the pipeline until this is done (Figure 16).

• Wear personal protective equipment when opening a blocked pipeline.

• Clear the area of nonessential personnel before opening the line.

• Plugs will be found in (in the order of likelihood) reducers, hoses, elbows, and pipe.

• If you are tapping the pipe to find the plug, the sound will be a dull thud (tik- tik) rather than a ringing sound (tong-tong) at the spot of the plug, because the jammed material will keep the pipeline from vibrating. (This method won’t find a plug in a hose.)

NO!

Figure 16

Never open a pressurized pipeline

6.16                                             WARNING   It is possible that some pressure will remain in the pipeline after reversing the pump. Use a shovel or pry bar to open the clamps on a blocked pipe- line. Wear face protection, and turn away from the pipeline when opening the clamp.

6.17                                             WARNING   It would be better to let the pipe be ruined by setting concrete than to risk injury by ignoring safe procedures. Always use safe practices when cleaning pipe. Remember, pipeline is replaceable, you are not.

6.18                                             WARNING   Do not kink hoses. Kinking will cause the pump to create max- imum concrete pressure. The pump may unkink the hose with force! (See Fig- ure 17.)

hosekinkcolor.eps 	hosepop3.eps

NO!

Do not allow

the hose to kink!

Figure 17

Kinking the hose creates a hazard

6.19                                             WARNING   Never use compressed air to clear a blockage! It is unsafe and unnecessary. The pump can develop much more pressure than an air compressor. If the pump pressure can’t move it, air pressure won’t either.

6.20                                             WARNING   Never stand on, sit on, or straddle a pipeline while it’s in use, or whenever it is pressurized. Pipeline wears out with each stroke of the pump. If the pipe bursts, you want to be to the side of it, not on top of it (Figure 18).

NO!

Figure 18

Never straddle or sit on a pressurized pipeline

pipelineguyColor.eps

6.21                                             WARNING   Crushing/amputation hazard. Do not remove the water box cov- ers or grates when the machine is stroking (Figure 19). If you must remove the water box cover (to add water, for example), and there is not a bolt-down grate over the water box, then stop the pump, take the transmission out of gear, so the pump cannot be restarted until you are finished and the covers are back in place. If a bolt-down grate is installed, you may simply stop the pump from stroking before removing the water box covers. Replace the covers before restarting the pump.

NO!

Figure 19

Keep your body out of the waterbox

6.22                                             WARNING   Never  leave  the  pump  unattended!  Before  you  leave  a laborer, ready mix driver, or any other worker alone with the pump for any reason, make sure the worker who you leave with the pump knows:

• the safety rules for a person stationed at the pump (the rules are listed in this

Safety Manual, beginning on page 39)

• how to stop the pump

• the location of the emergency stop switches

• how to signal you.

6.23                                             WARNING   To prevent any unintentional movements of the machine, all control devices on the operator’s panel and the remote control box must be switched off before changing from remote control to local control, or vice-versa. Whenever you are connecting or disconnecting the remote cable, push in the emergency stop button.

6.24                                             WARNING   Crushing/amputation hazard. Never put your hands, feet, or any other body part into the water box, concrete valve, or hopper when the hydraulic system is operational or ready to operate! (See Figure 20.)

NO!

Figure 20

Don’t put your body in the machine

NO!

safehopcolor.eps

6.25                                             WARNING   Do not work on the hopper, water box, concrete valve, or the hydraulic system unless the drive engine is turned off and the accumulator pres- sure (if so equipped) has been released! On units with internal combustion engines, the key must be removed. If there is more than one key, you should tag the ignition. On units driven by electric motors, the main disconnect must be locked out according to applicable standards.

6.26                                             WARNING   Never operate the pump “blind.” If you can’t see the point of placement, you must establish a system of communications with the workmen who can see the point of placement. Arrange for radio communications, a system of visual or auditory signals (lights or bells), or a spotter. If a spotter is used, agree on hand signals before beginning the pour! (Use of the ACPA standardized hand signals is highly recommended.)

7.  Safety Rules For Shotcreting

7.1                                        Keep the pump clean. A clean machine runs more safely and efficiently. To enhance the cleaning of your pump it will help to spray some type of bond breaker on the entire unit before each use (form oil or equivalent).

7.2                                               WARNING   The nozzle man and those working near him should always protect themselves by wearing appropriate safety gear, including a full face shield to prevent rebounding concrete from injuring their face and eyes (Figure 21).

faceshield.eps

Figure 21

Wear a full face shield for rebound protection

7.3                                               WARNING   Always direct the reducers away from the operator and the con- crete mixer driver. The line pressures are always very high during the shotcrete process (Figure 22).

Figure 22

Always point reducers away from the operator and driver

reducerangle.eps

7.4                                        If possible, the nozzle man and the pump operator should use radios to communi- cate with each other to facilitate a fast shut down in the event of a line plug.

7.5                                               WARNING   If setting up on a city street or some other obstacle prevents you from directing the reducers away from your work station, it can be helpful to use rubber matting and bungee cords to cover the reducers and act as a protective cover to protect you and the mixer driver in the event of a line rupture (Figure 23).

Figure 23

Cover reducers and use containment boxes for cleanout

reducercover.eps

7.6                                               WARNING   Crushing/amputation hazard! Always keep the hopper grate in place (Figure 24). Never put your hands, feet, or any other body part into the con- crete valve, hopper, or water box when the hydraulic system is operational or ready to operate! Never stand on the hopper grate!

Figure 24

Never remove the hopper grate while the pump is operating

Do Not remove the hopper grate while pumping!

grateoff.eps

7.7                                            CAUTIONOverspray  always presents a serious problem during the shotcrete process. Always protect personnel and equipment in the area by providing over- spray protection. Even when you are shooting on the inside. The most commonly used protection is plastic sheeting. It is easy to work with and can be nailed or fas- tened to almost any surface. Canvas tarps can be used in the same manner, but need to be cleaned frequently. Masonite and plywood also work well in some instances. It can help to over-form the area where shotcrete is to be applied. For example, if a wall is to be six feet high, you can form it to eight feet creating a two foot area of protection. The same would apply to the end of a wall.

7.8                                               WARNING   Always check all forms and rebar for stability, both backward and forward, before shotcrete is placed. The rebar cage needs to be tied to some- thing, usually the back form. When the shotcrete wall is being built up, the placed shotcrete wants to sag forward, bringing the rebar with it. If the rebar moves it is very likely that the form moved as well.

IV. Cleaning The Pump And System

8.  Safety Rules For Cleaning The Concrete Valve & Hopper

8.1                                               WARNING   Wear protective clothing and equipment when cleaning the con- crete pump because the lime in concrete can burn your skin. Protect against con- crete burns and concrete poisoning by wearing rubber boots and gloves during cleanout or any other time that you will be in contact with the concrete.

8.2                                               WARNING   Crushing and amputation hazard! Never put your hands or any other body part into the concrete valve. Instead, use water jets and the sup- plied rake (Figure 25).

8.3                                               WARNING   Never put your hands or any other body part into the machine when the hydraulic system is operational. If you must remove the grate to chip at hardened concrete, you must first disable the system by taking the transmission out of gear and locking the cab door, or stopping the engine, reliev- ing pressure in the accumulator circuit (if so equipped) and securing the controls against unintended operation. Reinstall the grate before restarting the engine (Fig- ure 25).

NO!

NO!

safehopcolor.eps

Figure 25

Keep your body parts out of the machine

9.  Safety Rules For Cleaning The Water Box

9.1                                               WARNING   Crushing  and  amputation  hazard!  Stop  the  concrete  pump before removing the water box covers. If your unit has bolt down guards, do not remove them for cleaning. If there is not a bolt-down guard over the water box, then stop the pump, take the transmission out of gear, and lock the cab so the pump cannot be restarted until you are finished cleaning and the covers are back in place. If a bolt-down grate is installed, you may simply stop the pump from stroking before removing the water box covers. Replace the covers before restart- ing the pump.

9.2                                               WARNING   Falling hazard! Be sure of your footing when cleaning the water box.

9.3                                               WARNING   Crushing and amputation hazard! Do not remove the water box guards for cleaning. Clean the water box with water jets only. Do not put your hands or any other body part into the water box for cleaning, or at any other time when the hydraulic system is operational.

NO!

Figure 26

Keep your hands out of the waterbox

10. Safety Rules For Cleaning A Separately Laid Pipeline

10.1                                             WARNING   Flying particle hazard! Clear the discharge area of personnel and equipment before forcing a ball or go devil through the pipeline, even if you are cleaning with water. Some air will be trapped in the pipeline, and the trapped air will become compressed before discharge.

10.2                                             WARNING   Using compressed air to clean the delivery system should only be done when no other method is practical or as recommended by the manufac- turer.

10.3                                             WARNING   The point of discharge must be controlled. Use a ball catcher or some other containment device at the point of discharge, even when cleaning with water.

Figure 27

Cleaning with compressed air can be extremely hazardous if you don’t follow the safety rules

confacegy2.eps

10.4                                             WARNING   If you have to use compressed air for cleaning the line you must have all of the necessary accessories. Read and understand the complete safety rules regarding cleaning out with compressed air in this section of the Safety Manual starting at paragraph10.8 on page 30. Cleaning with compressed air should only be done by qualified people.

10.5                                             WARNING   If the ball or go devil doesn’t come out of the delivery system after applying compressed air, you must relieve the pipe of air pressure before opening it. If the bleed off valve plugs when you are draining the air, the only safe way to proceed is to drill small holes into the pipeline, which will then allow the air to escape. Wear a full face shield when drilling the holes. Pipe you have drilled into is ruined and must be replaced. Drill the holes to relieve the air pressure even if the concrete has set up in the pipe. The pipe is hazardous until the pressure is relieved.

10.6                                             WARNING   Exercise care when “tapping” on the pipeline to find the loca- tion of the cleanout ball. Applying too much force will dent a single wall pipe (making it weak and unsafe) and could break the carbide insert of double wall pipe.

10.7                                             WARNING   It is better to let the pipe be ruined by setting concrete than to risk injury by ignoring safe procedures. Remember, pipeline is replaceable, you are not.

10.8	WARNING  Blowing out with compressed air creates potential hazards!

Serious injury or death could result if you do not adhere to these safety points.

• Blowing out must be performed under the supervision of a qualified per- son. (See the glossary for the definition of qualified person.)

• Blowing out requires two people! One trained person must be at the inlet end to operate the air insertion, and the other trained person must be near (but safely back from) the discharge point to monitor the discharge and to make sure that no one enters the hazard area.

• No pipe bends or flexible delivery hoses may be connected to the end of the pipeline during the blowing out process, unless there is a pre-planned cleanout station erected to route the discharge into the ready mix truck.

• The point of discharge must be controlled. Clear the discharge area of personnel and equipment before beginning the blowing out process. Do not allow anyone to enter the area during the blow out process. If a ball catcher is used, be aware of which type you have, and adjust your procedure accord-

ingly. Ball catcher types are described in paragraph 5.23 on page 17.

• The concrete outlet must be positioned high enough to permit easy dis- charge of the material.

• If you are going to divert the discharge into a discharge pipe system, you must lubricate the discharge line with slurry, or a plug could occur.

• The pipe cleaning blow out head must be equipped with a properly sized air discharge regulator valve and a separate water/air inlet. The two openings should be spaced apart far enough that a blowout ball could not cover both openings at once (Figure 28).

Water/air inlet

Air inlet regulator valve

Air discharge regulator valve

Figure 28

Ball catcher and blow out head

blow out head

ball catcher

• The plug or go devil must be thick enough to prevent compressed air flow around the plug into the concrete.

• The  pipeline must  not  be  disassembled until  it  has  been  completely relieved of air. Be sure of this! (See Figure 29.)

explode2col.eps

NO!

NO!

Figure 29

Never open a pressurized pipeline

•  Do not use compressed air to blow out concrete delivery hose, single pipe sections and short pipelines up to a length of 40 feet. Hoses will jump and move unpredictably; short pipelines don’t have enough concrete to resist the force of the air, causing it to discharge too quickly, like a cannon (Figure 30).

• When air pressure begins to drop rapidly, shut off the air supply from the compressor, and immediately begin bleeding air out of the pipeline. (The drop in pressure signifies that the pipeline is almost empty of concrete.)

hosepop3.eps

Figure 30

Never use air to blow out hoses or short pipelines

10.9		WARNING   When blowing out a vertical line, a shutoff valve is required to prevent the following scenario.

1.   (See diagram A in Figure 31.) Without a shutoff valve installed, the pipeline is disconnected from the pump. Immediately, the concrete drains out of the ver- tical sections of pipe, leaving concrete in both horizontal sections, and air trapped in between.

2.   (See diagram B in Figure 31.) The ball is inserted, and pushed with com- pressed air. This also compresses the air that is trapped in the vertical sections of pipe. The trapped air will be violently expelled when it reaches the end of the pipe, but the pipe will not yet be empty.

A shutoff valve installed at the bottom of the vertical run will prevent this hazard- ous situation. The shutoff valve must be capable of handling the maximum con- crete pressure of the pump and, of course, must be installed before the pour begins. Several different styles are available, ranging from a manually operated flat gate that is put into place with a hammer to fully hydraulic types that will also divert the concrete to a different pipeline. With a shutoff valve installed, you can proceed as indicated below.

blrt&wr2.eps

A	B

WRONG

5

2

C	D

1	4

3

Figure 31

Blowout of a vertical line

10.10		WARNING   Blowing out vertical sections of pipe (for example on a high rise building) requires additional safety precautions.

1.   Know where the discharge area for blowing out will be before the pour begins. Ready the area and accessories before the pour begins so you will not waste time when pumping is completed.

2.   Blowing out with compressed air requires two qualified persons.

3.   The persons at both ends of the pipeline must be able to communicate without delays, which means you must establish communications (for exam- ple, with a radio).

4.   When pumping is complete, close the shutoff valve before disconnecting the pipeline from the pump (item 1, Figure 31). Failure to do this will cause the concrete to fall out of the vertical sections of pipe, leaving concrete in the horizontal sections of pipe and an air pocket in the vertical sections. This does not apply if you are using a switching (diversion) valve.

5.   Install the ball(s) in the pipeline, secure the blow out head and hook up the air compressor. Do not apply the air yet! (Item 2, Figure 31.)

6.   If you will be diverting the discharge to a cleanout area, lubricate the dis- charge line with slurry, or a plug could occur.

7.   Position the ready mix truck at the cleanout standpipe, or install the ball catcher or other containment device at the end of the discharge line. (Item 3, Figure 31.)

8.   Clear the discharge area of personnel. You must allow no one to enter the discharge area until the pipeline is depressurized.

9.   Divert the vertical pipe line to the clean out area and secure the discharge (Figure 32), or open the shutoff valve in the delivery pipe line now. Allow gravity to start the concrete moving through the discharge line. As the con- crete falls from the vertical sections, it will take the ball with it, making it impossible to trap air in the line. (Item 4, Figure 31.)

Figure 32

divertcleanout.eps

Divert vertical pipeline to the cleanout area and be sure to secure the discharge before continuing

10. Apply the compressed air to the pipeline. Close communications must be maintained at this time. Add only enough air to keep the concrete moving. Do not allow the concrete to accelerate. (Item 5, Figure 31.)

11. When concrete starts to accelerate, shut-off the air supply from the com- pressor, and open the air regulator to bleed air from the line. Rapidly accelerating concrete indicates that the pipeline is almost empty. After the ball has been expelled from the pipeline, leave the air regulator open to be sure that all air is removed from the system.

12. All the rules for blowing out found in point 10.8 on page 30 also apply to blowing out a vertical pipe line. These rules are in addition to the general “cleaning a pipeline with compressed air” rules.

10.11                                           WARNING   Never use compressed air to attempt to clear a blockage! It is unsafe and unnecessary. If the pump pressure can’t move it, air pressure won’t either.

V. Maintenance Of The Machinery

11. Safety Rules Regarding Inspection

11.1                                            WARNING    Visually inspect your unit each day before it is put into opera- tion. If any problem is found that will affect the safe operation of the pump, don’t use the pump until it is repaired!

11.2                                            WARNING    If  safety  decals are  faded, missing, damaged, or  otherwise unreadable, they must be replaced immediately. Contact the manufacturer of your unit to obtain replacements.

11.3                                            WARNING    If safety devices or guards are removed for inspection purposes, they must be replaced before someone uses the machine.

11.4                                            WARNING    Pay attention to the Operation Manual and manufacturer’s ser- vice bulletins regarding maintenance and inspection procedures and intervals.

11.5                                            WARNING    If inspection reveals something that looks wrong, or even sus- picious, report it to the manufacturer for consideration. Don’t just assume that it’s OK.

11.6                                            WARNING    Visual  inspection of  the  concrete pump  circuits  and  safety devices should be done daily. Hands on inspection and documentation of results should be done weekly, or at least when preventive maintenance is scheduled.

11.7                                            WARNING    Do not neglect the delivery pipeline, clamps, or hoses. Check them often for wear, dents, and frays. Never send a unit to a job with a worn or damaged delivery system. For single wall pipes, ultrasonic thickness testers are more accurate than the tap method.

††

Figure 33

ultradwg.eps

Check delivery system wall thickness with an ultrasonic thickness tester

12. Safety Rules Regarding Scheduled Maintenance

12.1                                           WARNING    Proper and timely maintenance is important to the safe opera- tion of a concrete pump. The proper procedures are outlined in the Operation Manual supplied with the pump. Do not put it off. Do not treat it lightly. Do not “fudge” results. The lives of the operator, oiler, and workers on the job are depending on it.

12.2                                           WARNING    Keep the machine clean! Oil spills, grease, loose tools, and dis- placed accessories are hazards.

12.3                                           WARNING    Pins should be used on all delivery system clamps. Clamps that will hang over workers, and clamps used on system that will be dragged shall be pinned (Figure 34).

Figure 34

Pin the clamps

pinclmp.eps

12.4                                           WARNING    Be sure that you are installing the correct clamps for the types of pipe ends used. Never try to mate dissimilar pipe ends unless using a clamp specifically made for this purpose. See the comparison regarding weld-on ends on page 50 in the Appendix of this manual.

12.5                                           WARNING    When using new pipe and/or hose on the machine be sure that it is capable of handling the maximum concrete pressure of the pump. (removed text)

12.6                                           WARNING    If safety devices or guards are removed for servicing, they must be replaced before the machine is put back in service.

12.7                                           WARNING    Do not change the maximum relief valve setting on any hydrau- lic circuit without permission from the manufacturer. Never change an accumula- tor circuit pressure setting without specific instructions from the manufacturer.

12.8                                           WARNING    Never make unauthorized modifications to structural members or pressure circuits.

| 12.9 | WARNING | You must replace, not repair damaged hydraulic or concrete |
| --- | --- | --- |
|  | hoses or pipes. |  |
| 12.10 | WARNING | Never try to repair a machine using worn, damaged, or defec- |

tive components.

12.11                                      NOTICE    Never  allow  welding  current to  travel  through bearings or hydraulic cylinders. Keep the ground cable on the component that is being welded.

12.12	NOTICE	Electronic components can be destroyed by welding current.

Before welding on the unit, you must disconnect the battery cables, and unplug all radio remote control power wires. If in doubt, contact the Service Department of the manufacturer for instructions before proceeding.

13. Safety Rules When Servicing The Machinery

13.1                                           WARNING    Repairs should be carried out by qualified workshop per- sonnel (See the glossary for the definition of qualified personnel.)

13.2                                           WARNING    Read and understand the maintenance procedures in the Operation Manual of the machine before attempting any repairs. If in doubt, call the manufacturer. Incorrectly done repairs affect the safe use of the machine.

| 13.3 | WARNING | Burn hazard! Never work on a hot hydraulic system. |
| --- | --- | --- |
| 13.4 | WARNING | Falling hazard! If you cannot work at ground level, you must |

find and use a suitable work platform, a tie-off harness system, or otherwise

secure yourself from falling.

13.5                                           WARNING    If maintenance work requires that you use a crane, hoist, fork truck, or similar machine, read and understand the safety regulations for that equipment.

13.6                                           WARNING    Only  operators should  operate  the  unit.  If  work  on  the machine requires that it be operated and you are not qualified as an operator, you must get someone who is qualified to assist you.

13.7                                              DANGER   Electrocution hazard! Repair work on high voltage electrical systems must be done by qualified electricians. For this rule, high voltage means anything over 24 volts.

13.8                                           WARNING    Explosion hazard! Be sure that you understand the potential danger of spring loaded or compressed gas components before you service them. (Examples: nitrogen accumulators, gas springs for toolbox doors, tires, brake chambers.) If you don’t know the dangers, call the manufacturer before beginning work!

13.9                                           WARNING    If you will be working in a hidden area inside the machine, lock it out as follows.

• With a gas or diesel engine, remove the ignition key and place a Do Not Oper- ate sign on the controls. Carry the key with you.

• With an electrically driven pump, lock out the main breaker and tag the con- trols.

The above rules are one simple “Lock Out-Tag Out” procedure. A procedure may also be provided in the operation manual for the unit and there may be state or local regulations that require a more advanced or stringent Lock Out-Tag Out pro- gram. Be aware of the regulations in your area.

13.10                                         WARNING    Never activate the system hydraulics without checking if another workman is in a hidden position. Always yell “clear” before starting the engine or electric motor, and allow time for response.

13.11                                          WARNING    Never work on a pressurized hydraulic system. Stop the engine or electric motor and relieve the accumulator circuit (if so equipped) before you open the hydraulic system.

13.12                                         WARNING    Never use gasoline or diesel fuel as a cleaning solvent. This is critical to remember when cleaning hydraulic oil reservoirs, because gas and diesel fuels are highly explosive and traces left in the oil may ignite when com- pressed!

13.13                                         WARNING    Remember to mount and dismount the unit using the “3 Point Rule.” One hand and two feet or two hands and one foot are to be in contact with a secure surface at all times (Figure 35).

safestep.eps

Figure 35

The 3 Point Rule

13.14		WARNING	Always use the correct tools for the job. Tools should be kept clean and in good condition.

13.15		WARNING	If you see a co-worker engaging in an unsafe  practice, warn him about the dangers. Safety is always in the hands of those on the job!

13.16		WARNING	After any repair is completed, test the function of the repaired part to be sure that repairs were done correctly.

VI. Co-worker Safety

14. Safety Rules For Workers Assigned To The Pump.

14.1		WARNING   You must know how to stop the pump. Have the operator show you the locations of the emergency stop switches (Figure 36).

E-Stop Switch

WARNING

DANGER

Stay clear.

Contact will result in

Stop  agitator before putting any solid object in hopper.

WARNING

of hopper and

This machine is remote controlled

WARNING

death or serious injury

and may start at any       Keep hands out

if the unit becomes

time.  Stop engine

valve assembly. See operation

electrically charged.

before servicing unit.      manual if access

is required.

Figure 36

Know how to stop the unit in an emergency

estop.eps

14.2                                             DANGER    You should wear the same personal protective equipment as the operator. Goggles, hard hat, ear protection, and rubber gloves are especially important when working near the hopper (Including *full face shield or * breath- ing mask where necessary, as shown in Figure 37)

*   Breathing mask needed when cement dust (or other toxic dust) is present in the air.

*  Full face shield is needed when shotcreting or any time material being placed is rebounding.

Figure 37

Wear the same personal protective equipment as the operator

ready mix truck and the pump! Stand to the side, where the driver can see you

(Figure 38).

NO!

Figure 38

bkupguy.eps

Never stand between the ready mix truck and the pump

14.4		WARNING	When backing in ready mix trucks, use clear and concise hand signals (Figure 39).

Figure 39

Use clear, concise hand signals

Clear Signals

YES!

clearsig.eps

14.5                                             WARNING   If handling the chutes of a ready mix truck, keep your hands clear of the hinged areas.

14.6		WARNING	Do not allow the ready mix driver to put concrete in the pump hopper until the pump operator gives him the OK. Filling the hopper early can cause the pump to plug.

14.7                                           WARNING    If you see foreign material that could create a blockage coming from the ready mix truck, alert the operator to stop the pump. Do not attempt to remove the material from the hopper or grate while the hydraulic system is ready to work. (See point 14.16 on page 43.) If necessary, depress the E-stop button to stop the pump and alert the operator.

14.8                                           WARNING    Never allow the ready mix driver to clean out in the hopper, because it can create a blockage. (Water will wash the cement and fine sand from the course aggregate causing segregation.)

14.9                                           WARNING    Do not operate the pump unless you are also a trained operator and the regular operator has released the controls to you. There must not be more than one operator at a time. This does not apply to stopping the pump or boom if there is a need to do so.

14.10                                         WARNING    Do not let the concrete level in the hopper become low! If air is sucked into the material cylinders, the pump will compress the air. Compressed air always poses a hazard as it is expelled from the hopper or the delivery pipeline (Figure 40). If air is taken into the material cylinders, take the following steps to minimize the hazard:

1.   Stop the pump immediately. Hit the emergency stop button if that is the quickest way to stop the pump. There will be an expulsion of compressed air the next time the concrete valve shifts. If possible, fill the hopper with concrete to help contain the expulsion. Do not put your face directly over the hopper.

2.   Alert the operator of the problem. It is his job to know the procedures for safe removal of air from the pump and delivery system. These procedures include pumping in reverse for a couple of strokes.

3.   Persons standing at the discharge end or near the delivery line must be warned to move away until all of the air has been purged. Warn them to stay a reasonable and prudent distance beyond the reach of the end hose or point of discharge (Figure 40).

4.   When the pump is restarted, don’t assume that the first little air bubble is the end of the compressed air.

5.   Do not allow anyone near the discharge until concrete runs steadily from the end and there is no movement of the delivery system.

• If workers are positioned in high or precarious places, warn them to expect a loud sound as the air escapes the pipeline. (Warn them even if they are well away from the discharge.) That way, we can prevent the worker from falling as a result of being startled by the noise.

hosepop3.eps

Figure 40

Remove everyone from the discharge area whenever the pump is first starting, restarting after moving, or if air has been introduced into the line

after moving, when restarting after adding or removing hoses, or whenever air has

been introduced into the line, warn everyone to stay away from the discharge until concrete runs steadily and there is no movement of the delivery system. Personnel should stay back a reasonable and prudent distance beyond the reach of the end hose or point of discharge (Figure 40). Air will be in the line when first starting, when restarting after moving, when a blockage has been successfully removed by “rocking” the concrete, and after the line has been taken apart or opened for any reason.

14.12                                         WARNING    Never use compressed air to clear a blockage! The operator is responsible for knowing the safe blockage removal procedures. It is unsafe and unnecessary to use compressed air. If the pump pressure can’t move it, air pres- sure won’t either.

14.13                                         WARNING    Never stand on, sit on, or straddle a pipeline while it’s in use, or whenever it is pressurized. Pipeline wears out with each stroke of the pump. If the pipe bursts, you want to be to the side of it, not on top of it (Figure 41).

NO!

Figure 41

Never straddle or sit on a pressurized pipeline

pipelineguyColor.eps

14.14                                         WARNING    Expulsion hazard! Never open a pipeline that is under pres- sure (Figure 42). The pump must be run in reverse for at least two strokes and then stopped before opening a pipeline. If the pipeline is pressurized with air, do not open it. The operator is responsible for knowing how to safely release the air pressure.

explode2col.eps

NO!

NO!

Figure 42

Never open a pressurized pipeline

14.15	WARNING	Be careful when handling pipeline or any other heavy object.

Learn how to lift without using your back. Get assistance if needed.

14.16                                         WARNING    Crushing/amputation hazard! Never put your hands, feet, or any other body part into the water box, concrete valve, or hopper when the hydraulic system is operational or ready to operate! Never stand on the hopper grate! (See Figure 43.)

NO!

Figure 43

Never put your body in the machine!

NO!

safehopcolor.eps

14.17	WARNING	Never lift or remove the hopper grate for any reason (Figure

44).

Figure 44

Lifting hopper grate exposes the agitator and the concrete valve

agitguy.eps

14.18		WARNING	Do not remove the water box covers or grates when the machine is stroking (Figure 45). Do not remove the water box cover (to add water, for example), until the operator has disabled the machine. Replace the covers before the operator restarts the pump.

Figure 45

Do not remove the water box covers when the machine is stroking

NO!

donotrem.eps

14.19	WARNING	Mount or dismount the pump or truck using the 3 Point Rule.

One hand and two feet or two hands and one foot are to be in contact with a secure surface at all times (Figure 46).

Figure 46

The 3 Point Rule

safestep.eps

14.20	WARNING	Keep unauthorized personnel off of the pump.

15. Safety Rules For The Placing Crew

15.1                                           WARNING    Wear Personal Protective Equipment (P.P.E.) when working around a concrete pump (Figure 47). The gloves should resist concrete lime burns. If you will be working in the concrete, protect your feet and hands with rubber boots and gloves (including *full face shield or * breathing mask where necessary, as shown below).

Figure 47

Wear Personal Protective

Equipment (P.P.E.)

15.2                                           WARNING    When the operator is initially priming the delivery system, restarting after moving, restarting after adding or removing pipes or hoses, or any time that air has been introduced into the delivery system, stand a reasonable and prudent distance away from the tip hose or point of discharge. Do not get near the discharge until material runs steadily and there is no movement of the delivery system. (Figure 48). Compressed air in the line can cause rubber hose to move violently. If the operator tells you that air is coming in the delivery system, pro- ceed as follows:

• Get to ground level (if in a high place) and remain well away from the dis- charge or at least take cover.

• Stay away from the discharge. Be sure that all the air is gone before getting near the point of discharge again. It is the operator’s job to know when it’s safe to go back to normal pumping.

hosepop3.eps

Figure 48

Stay away from the point of discharge when starting or restarting, and when there’s air in the pipeline

15.3                                           WARNING    Never use compressed air to clear a blockage! It is unsafe and unnecessary. If the pump pressure can’t move it, air pressure won’t either. Stand away from the discharge and the line if anyone attempts to use compressed air in this manner.

| 15.4 | WARNING | Do not look into the end of a plugged hose or pipe! |
| --- | --- | --- |
| 15.5 | WARNING | When the pump crew is using compressed air to clean the boom |

or system pipeline, stay away from the discharge area. Never try to hold down a

pipe or hose that is being cleaned with air.

15.6                                           WARNING    Never open a pressurized pipeline (Figure 49). The pump oper- ator must release the pressure before you open the line. If the line is pressurized with compressed air, let the operator release the pressure and verify that the air has escaped before you proceed.

explode2col.eps

NO!

NO!

Figure 49

Never open a pressurized pipeline

15.7		WARNING	After removing pipe sections you must reassemble using gas- kets and clamps. Pipelines assembled without gaskets will leak cement and water, which can cause a blockage.

15.8                                           WARNING    Concrete is being moved through the delivery system by pres- sure. Failure of a pipe, clamp, hose, or elbow is possible. For this reason, spend as little time as possible standing near the pipeline, and wear protective clothing.

15.9		WARNING	Do not kink the end hose. Kinking will cause the pump to cre- ate maximum concrete pressure. The pump may unkink the hose by force! (See Figure 50.)

hosekinkcolor.eps

NO!

Do not allow

the hose to kink!

Figure 50

Never kink the hose; Never hold the hose with your shoulder

15.10	 	CAUTION    Be careful when handling pipeline or any other heavy object.

Learn how to lift without using your back. Get assistance if needed.

15.11		WARNING	Falling hazard! When pouring columns, slabs, or walls above ground, secure yourself from falling.

15.12                                         WARNING    Never stand on, sit on, or straddle a pipeline while it’s in use, or whenever it is pressurized (Figure 51). Pipeline wears out with each stroke of the pump. If the pipe bursts, you want to be to the side of it, not on top of it.

NO!

Figure 51

Never straddle or sit on a pressurized pipeline

pipelineguyColor.eps

15.13		WARNING	To avoid confusion and conflicting signals, only one person should signal the pump operator except for the stop signal.

15.14		WARNING   Before the pour begins, the hose man and the operator should agree on the hand signals (Figure 52).

(2 taps)

1.

START PUMP

2.

SLOW PUMP

3.

STOP PUMP

4.

LITTLE BIT

5.

RELIEVE

6.

ADD WATER

7.

ALL DONE

SPEED UP

DOWN

PRESSURE

4-GALLONS

CLEAN UP

ACPAhandsigsmallline.eps

Figure 52

Recommended ACPA hand signals